BubbleCopter
- Arduino powered location aware quadcopter
- Raspberry Pi powered 360º video recording
- Original goals:
  - <£200 build cost
  - >30 minutes flight time
  - >500m control range
  - GPS based autopilot
  - >15 FPS video captured at >1000x1000px

---
360º Photography
- Using BubbleScope mobile phone attachment
- Ideal capture resolution is an image in 1:1 aspect ratio
- Majority of capture is what is around the BubbleScope rather than what is above or below it

---
360º Photography
- Using Raspberry Pi and camera board
- Other options considered:
  - BeagleBone Black with USB webcam (limited V4L2 driver)
  - ODROID with USB webcam (limited by camera capture modes)
- BubbleScopeCL tool
  - Allows capturing still images, videos and timelapses from a V4L2 source in either original or unwrapped format
  - Can unwrap pre recorded video, stills and timelapse frames
  - Can be used with MJPEG-Streamer to stream video from a capture source
- Current method of capture on BubbleCopter
  - Record H264 video, JPEG images or timelapse frames using raspicam tools controlled through GPIO via the flight controller
  - Get recorded data from Raspberry Pi SD card
  - Convert recordings on PC

---
Multirotor Design
- Typically range from 3-8 rotors
- More rotors
  - Greater stability
  - More lifting capability
  - Expensive
  - Tolerant of in flight motor/propellor failures
  - Typically used for stable aerial imaging and carrying significant payloads
- Less rotors
  - More maneuverability
  - Lower power consumption
  - Cheaper
  - Typical off the shelf or self built multirotor

---
Frame and Drive Electronics
- Custom designed frame
  - 6mm laser cut MDF
  - 3mm MDF panels to hold some electronics, Pi and BubbleScope
  - Various 3D printed and laser cut parts to hold individual components
- Off the shelf drive electronics
  - Trunigy 4 cell 5Ah Lithium Polymer battery
  - Trunigy 1000KV brushless DC motors
  - Turnigy 40A ESC motor drivers

---
Flight Control
- Multiple modes of operation:
  - Navigation
    Aware of geographic position
  - Restorative Stabilisation
    Revert to target flight attitude
  - Balancing
    Attempt to maintain current flight attitude
- Can be broken into three main components:
  - Sensing the current state (“Knowing where you are”)
  - Knowing how to react to the state to achieve a desired outcome (“Knowing what to do”)
  - Being able to react to the state (“Knowing how to do it”)

---
Knowing where you are
- Gyroscope
  - Measures angular velocity (rad.s-1)
  - Used for vehicle balancing
- Accelerometer
  - Measures proper acceleration (g)
  - Used to restore vehicle attitude after being moved by an external force
- Magnetometer
  - Measures magnetic flux density (G)
  - Used to determine compass heading
- Barometric Altimeter
  - Measures altitude above sea level (ft)
- Ultrasonic Altimeter
  - Measures altitude relative to terrain up to 6m
  - Used for terrain referenced altitude hold and automatic landing
- GPS
  - Useful measurements: latitude, longitude and altitude
  - Used for autopilot (position hold, route follow, etc.)

---
Knowing how to do it
http://www.ni.com/white-paper/3782/en/

---
Knowing how to do it
- PID Control
  - Proportional Response
    - Calculate difference between target value and process value (the error term)
    - Used to compensate for the majority of the error
  - Integral Response
    - Sums error term of each iteration
    - Used to reduce steady state error to zero
  - Derivative Response
    - Measures rate of change of process value
    - Used to compensate output value for rapid changes in process value, hence reduces overshoot

---
Knowing how to do it
- PID in BubbleCopter
  - P calculated from difference between target pitch/bank angle and current pitch/bank angle (calculated from accelerometer and gyroscope)
  - I is ignored as target pitch/bank has no long term stable state
  - D is calculated using the values form the gyroscope
- Motor control
  - BubbleCopter uses the X4 multirotor configuration
  - Pitch and bank angles modified by adjusting throttle on pairs of motors
  - Yaw angle modified by adjusting throttle on pairs of motors running is same direction
    - Causing an overall rotational inertia on the vehicle about the Z axis

---
Knowing what to do
- Ground Transmitter
  - Radio link between operator and quadcopter
  - Requirements:
    - Range
    - Low latency
    - Durability
  - Current control method for BubbleCopter
- Autopilot
  - Usually GPS based
    - Can use a range of sensors to determine next action
  - Predefined flight plan programmed into flight controller before takeoff
  - Can include auto takeoff and landing with supporting sensors

---
More Information
github.com/DanNixon/BubbleCopter
github.com/DanNixon/BubbleScopeCL
@TechnoDucky
dan-nixon.com